## Slide 1: Center for Green Transport
Niels-Anders Nielsen Head of Center

## Slide 2: A green vision for DK
A long term strategy and a coherent plan for a sustainable transport system with high mobility
A three-leg strategy
  Implementation of green taxes on cars
  More and efficient public transport
  New sustainable technologies and a stronger research
Concrete cost-efficient actions to be imposed now

## Slide 3
Recommendation and guidance about public purchase of energy-efficient and eco-friendly vehicles
Certification of green communities and private transport companies
Energy rating of delivery vans
Eco-driving (campaigns and courses)
Continuation of tests of road trains
Optimizing the aerodynamic equipment on trucks
Energy requirements for taxis
Concrete initiatives to reduce
CO2-emissions

## Slide 4: Danish energy classes
Class | Petrol km/l | Diesel km/l
A | 18,2- up | 20,5- up
B | 15,4-18,1 | 17,3-20,4
C | 14,3-15,3 | 16,1-17,2
D | 12,5-14,2 | 14,1-16,0
E | 11,8-12,4 | 13,2-14,0
F | 10,5-11,7 | 11,9-13,1
G | 4,5-10,4 | 5,1-11,8
Used for cars since 2000.
Similar to the system known from white goods

## Slide 5: Part of the concrete initiatives under Center for Green Transport
Energy requirements for taxis
  The law is supported by all parties in the government
  The executive order was valid from September 15, 2009 with following requirements:
    Designed for max 5 adults: Energy class C
    Designed for 6-7 adults: Energy class D
    Designed for 8-9 adults: Energy class F
  Exceptions
    Taxis designed for 2 wheelchairs and fixed lift
    Limousines with extended wheelbase and classic cars
  Yearly validation and adjustment to the technologic development

## Slide 6: Energy classes for taxis
Class | Petrol km/l | Diesel km/l
A | 18,2- up | 20,5- up
B | 15,4-18,1 | 17,3-20,4
C | 14,3-15,3 | 16,1-17,2
D | 12,5-14,2 | 14,1-16,0
E | 11,8-12,4 | 13,2-14,0
F | 10,5-11,7 | 11,9-13,1
G | 4,5-10,4 | 5,1-11,8

## Slide 7: Grouping of existing taxis for 5 adults
4276 taxis, limousines and cars for transport of patient
designed fo five adults
12
55
521
1199
1545
632
312
0
200
400
600
800
1000
1200
1400
1600
1800
A
B
C
D
E
F
G
Energy rating
Picesl

## Slide 8: Status so far
Transitional provisions
If a contract was signed before July 1st, 2009 stating delivery before end of 2009, a dispensation is issued. So far 19 cars has been granted an exemption
Producer adjustments
Mercedes E-series can now be delivered with energy rating C

## Slide 9: Expectations
Today 75 % of the Danish taxis are designed for 5 adults
Hereof 7 % is energy class C – the rest is below
The expectation is that when all taxis are energy class C or better the trade will see a fuel reduction of 7 millions liters per year
Equal to 350 road tankers –
one per day

## Slide 10
Thank you for your attention